## Slide 1
Combining Machine Learning With Finite Element Simulations For Fast Computation In Power Module Failure Analysis Due to Wire Bond Degradation
Mehdi Ghrabli, Mounira Bouarroudj, Ludovic Chamoin, Emanuel Aldea
CNRS, SATIE & LMPS Laboratories

## Slide 2: OUTLINE
Introduction
Simulations and data generation
Regression results and analysis
Machine learning beyond regression
Conclusion

## Slide 3: INTRODUCTION
Context
Average lifetime 10 to 15 years when used for transportation
Aging caused by successive thermal loads
Power electronic module : Packaging (up) and interior view (down)

## Slide 4: INTRODUCTION
Context
Average lifetime 10 to 15 years when used for transportation
Aging caused by successive thermal loads
=> Unfeasible experimentally
=> Difficult to model due to variance
Loading profile of a power electronic module in an electric vehicle

## Slide 5: OUTLINE
Introduction
Simulations and data generation
Regression results and analysis
Machine learning beyond regression
Conclusion

## Slide 6: SIMULATIONS AND DATA GENERATION
Failure mechanism
Architecture of a power module
Component | Material
Wire | Aluminium
Chip | Silicon
Solder | Silver
Copper layer | Copper
Ceramic layer | Ceramic
Material composition of an IGBT power module

## Slide 7: SIMULATIONS AND DATA GENERATION
Failure mechanism
Architecture of a power module
Creation of thermal stress in the wire-chip interface

## Slide 8: SIMULATIONS AND DATA GENERATION
Failure mechanism
Architecture of a power module
Initiation of a crack due to subsequent loading

## Slide 9: SIMULATIONS AND DATA GENERATION
Failure mechanism
Architecture of a power module
Crack propagation

## Slide 10: SIMULATIONS AND DATA GENERATION
Failure mechanism
Architecture of a power module
Wire lift-off
Module’s state : Health indicator (Collector-emitter voltage)  Degradation (remaining contact area due to the crack)

## Slide 11: SIMULATIONS AND DATA GENERATION
Geometric model of the power module
Reduced geometric model of the power module
Geometric modelling

## Slide 12: SIMULATIONS AND DATA GENERATION
Reduced geometric model of the power module
Thermal loading
Current injection

## Slide 13: SIMULATIONS AND DATA GENERATION
Reduced geometric model of the power module
Thermal loading
Current injection
Self heating

## Slide 14: SIMULATIONS AND DATA GENERATION
Reduced geometric model of the power module
Thermal loading
Current injection
Self heating
Thermal stress in contact area

## Slide 15: SIMULATIONS AND DATA GENERATION
Reduced geometric model of the power module
Thermal loading
Current injection
Self heating
Thermal stress in contact area
Retrieve mechanical quantities : Equivalent total strain ɛ

## Slide 16: SIMULATIONS AND DATA GENERATION
Data generation
Temperature | Contact radius | Mech node coordinate | Mech node coordinate | Equivalent total strain ɛ
 |  |  |  | Equivalent total strain ɛ
Input
Output
Bounding inputs :
  
1000 simulations 3 minutes/sim
Inputs chosen using random uniform sampling

## Slide 17: OUTLINE
Introduction
Simulations and data generation
Regression results and analysis
Machine learning beyond regression
Conclusion

## Slide 18: REGRESSION RESULTS AND ANALYSIS
Results
Models/Metrics | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear |  |  |  |  | 
Regularization (linear) |  |  |  |  | 
Tree-based |  |  |  |  | 
Non-parametric |  |  |  |  | 
Neural network |  |  |  |  | 
Models/Metrics |  |  | R² | Fitting time (s) | Inference time (ms)
Linear |  |  |  |  | 
Regularization (linear) |  |  |  |  | 
Tree-based |  |  |  |  | 
Non-parametric |  |  |  |  | 
Neural network |  |  |  |  | 
Parameters estimated using cross-validation
70-30 training-test splits

## Slide 19: REGRESSION RESULTS AND ANALYSIS
Results
Models/Metrics | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Models/Metrics |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Regression results (best metric per column in bold, worst underlined)
Tree-based models perform the best across all prediction metrics

## Slide 20: REGRESSION RESULTS AND ANALYSIS
Results
Models/Metrics | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Models/Metrics |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Regression results (best metric per column in bold, worst underlined)
Tree-based models perform the best across all prediction metrics
Regularization has a slight detrimental effect (Linear/Random forest/dropout) due to the deterministic nature

## Slide 21: REGRESSION RESULTS AND ANALYSIS
Residuals
Residuals of the best performing model (Bagging) with respect to geometric features

## Slide 22: REGRESSION RESULTS AND ANALYSIS
Residuals
Peak strain near the contact tip ()
Reduce uncertainty using :
  Refining the meshing
  Data augmentation/balancing
Visualization of a simulation showing the equivalent total strain in the elliptic contact area

## Slide 23: REGRESSION RESULTS AND ANALYSIS
Visualization : Linear regression

## Slide 24: REGRESSION RESULTS AND ANALYSIS
Visualization : LASSO

## Slide 25: REGRESSION RESULTS AND ANALYSIS
Visualization : Ridge

## Slide 26: REGRESSION RESULTS AND ANALYSIS
Visualization : ElasticNet

## Slide 27: REGRESSION RESULTS AND ANALYSIS
Visualization : Polynomial (degree 4)

## Slide 28: REGRESSION RESULTS AND ANALYSIS
Visualization : Decision Tree

## Slide 29: REGRESSION RESULTS AND ANALYSIS
Visualization : Boosting

## Slide 30: REGRESSION RESULTS AND ANALYSIS
Visualization : Random forest

## Slide 31: REGRESSION RESULTS AND ANALYSIS
Visualization : Bagging

## Slide 32: REGRESSION RESULTS AND ANALYSIS
Visualization : Support vector regression

## Slide 33: REGRESSION RESULTS AND ANALYSIS
Visualization : k-Nearest neighbours regressor

## Slide 34: REGRESSION RESULTS AND ANALYSIS
Visualization : Neural networks

## Slide 35: OUTLINE
Introduction
Simulations and data generation
Regression results and analysis
Machine learning beyond regression
Conclusion

## Slide 36: MACHINE LEARNING BEYOND REGRESSION
Active learning
A machine learning approach that attempts to maximize a model’s performance gain while annotating the fewest samples possible
Uses model uncertainty to determine the most important sample to annotate

## Slide 37: MACHINE LEARNING BEYOND REGRESSION
Active learning : example

## Slide 38: MACHINE LEARNING BEYOND REGRESSION
Active learning : example

## Slide 39: MACHINE LEARNING BEYOND REGRESSION
Active learning : example

## Slide 40: MACHINE LEARNING BEYOND REGRESSION
Active learning : example

## Slide 41: MACHINE LEARNING BEYOND REGRESSION
Active learning : example
Highest uncertainty = most important to label

## Slide 42: MACHINE LEARNING BEYOND REGRESSION
Active learning : adaptation
Use an ensemble of (highest performing) predictors as the final model : combine Bagging, K-NN, Neural network
Select a pool of simulations to choose from
Predict the equivalent total strain using every predictor :
Calculate the variance of the ensemble )
Prioritize the simulations with the highest variance

## Slide 43: MACHINE LEARNING BEYOND REGRESSION
Active learning : results
Active learning using 50 test simulations, 50 initial training simulations and 500 pool simulations (fully utilized)

## Slide 44: MACHINE LEARNING BEYOND REGRESSION
Active learning : results
Active learning using 50 test simulations, 50 initial training simulations and 500 pool simulations (50% utilized)

## Slide 45: OUTLINE
Introduction
Simulations and data generation
Regression results and analysis
Machine learning beyond regression
Conclusion

## Slide 46: CONCLUSION
Takeaways
Machine learning models give plausible results when used as surrogate models for finite element models in power module’s reliability assessment
Tree-based models have the best statistical properties due to their decision-based regression, with K-NNs being competitive statistically and computationally
Residuals can guide the user in the data selection and generation process
Active learning improves convergence time and increases accuracy by choosing iteratively the best numerical simulations to carry out

## Slide 47: CONCLUSION
Improvements and future work
Transfer learning is an interesting approach to tackle the problem of complex and scarce simulations
The effect of meshing can be the topic of future work to optimize computational time and improve accuracy
Uncertainty should be quantified, and machine learning should be used with caution for applications with a high risk and a limited margin of tolerance

## Slide 48
Thank you for your attention!
mehdi.ghrabli1@ens-paris-saclay.fr
Contact :
github.com/MehdiGhrabli/ML4FE
Project repository :
github.com/MehdiGhrabli/PIMC4RUL
Related :

## Slide 49: REFERENCES
[1] T. Hunger et al. Surge current limitations. Power systems design, 2011. https://www.powersystemsdesign.com/articles/surge-current-limitations/22/5852
[2] Thoben, M. & Mainka, Krzysztof & Bayerer, Reinhold & Graf, I & Münzer, M. (2008). From vehicle drive cycle to reliability testing of Power Modules for hybrid vehicle inverter.
[3] N. Dornic. Elaboration et comparaison de deux modèles de durée de vie des fils d’interconnexion des modules de puissance, l’un base sur les déformations et l’autre sur les dégradations. PhD thesis, Université Paris-Saclay, 2019.
[4] Camille Durand, Markus Klingler, Coutellier Daniel, and Hakim Naceur. Powercycling reliability of power module: A survey. IEEE Transactions on Deviceand Materials Reliability, 16:1–1, 03 2016.
[5] Hichem Felouat, Transfer learning Keras & TensorFlow. 2020.

## Slide 50: MACHINE LEARNING BEYOND REGRESSION
Transfer learning
A machine learning technique that involves utilizing knowledge learned from one task to improve performance on another related task.
Beneficial when the second task is related to the first and/or when data for the second task is scarce

## Slide 51: MACHINE LEARNING BEYOND REGRESSION
Transfer learning : example
Task 1 : Image recognition of cats
  Accessible data, easy to train models
Taks 2 : Image recognition of tigers
  Limited data, hard to train models
Solution : Use transfer learning to share knowledge (Feature detection of whiskers, eyes, ears) from task 1 to task 2

## Slide 52: MACHINE LEARNING BEYOND REGRESSION
Transfer learning : Application
Task 1 : Surrogate model used on simplified geometry
  Accessible data, easy to train models
Taks 2 : Surrogate model used on complex geometry
  Limited data, hard to train models
Solution : Use transfer learning to share knowledge (Geometric features, relationship between node values) from task 1 to task 2

## Slide 53: SIMULATIONS AND DATA GENERATION
Data generation
Load | Contact radius | Mech node coordinate | Mech node coordinate | Equivalent total strain ɛ
 |  |  |  | Equivalent total strain ɛ
Input
Output

## Slide 54: SIMULATIONS AND DATA GENERATION
Data generation
Temperature | Contact radius | Mech node coordinate | Mech node coordinate | Equivalent total strain ɛ
 |  |  |  | Equivalent total strain ɛ
Input
Output

## Slide 55: SIMULATIONS AND DATA GENERATION
Reduced geometric model of the power module
Geometric modelling
Truncated cone representing the elliptical contact area

## Slide 56: INTRODUCTION
Remaining useful life estimation
Pointwise estimation
Simple model
Quick inference (estimation at the initial state)
Restricting assumptions
Coffin-Manson law

## Slide 57: INTRODUCTION
Remaining useful life estimation
Pointwise estimation
Sequence-based estimation
Simple model
Quick inference (estimation at the initial state)
Restricting assumptions
Complex model
Slow inference (estimation after every loading cycle)
Robust to load variation
Coffin-Manson law
Paris’ law

## Slide 58: INTRODUCTION
Remaining useful life estimation
Pointwise estimation
Sequence-based estimation
Simple model
Quick inference (estimation at the initial state)
Restricting assumptions
Uses feedback loops (health indicator + finite element model)
Coffin-Manson law
Evolution of the health indicator with respect to the number of loading cycles

## Slide 59: INTRODUCTION
Remaining useful life estimation
Pointwise estimation
Sequence-based estimation
Simple model
Quick inference (estimation at the initial state)
Restricting assumptions
Uses feedback loops (health indicator + surrogate machine learning model)
Coffin-Manson law
Evolution of the health indicator with respect to the number of loading cycles

## Slide 60: REGRESSION RESULTS AND ANALYSIS
Interpretation : Linear model
 | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Polynomial model (degree 4) | 0,66 | 1,161 | 0,857 | 2,032 | 8,780
 |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Polynomial model (degree 4) | 0,66 | 1,161 | 0,857 | 2,032 | 
Regression results (best metric per row in bold, worst underlined)
Parameters estimated using cross-validation
70-30 training-test splits

## Slide 61: REGRESSION RESULTS AND ANALYSIS
Interpretation : Regularization
 | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Ridge | 1,851 | 2,329 | 0,6 | 1,891 | 0
Lasso | 1,851 | 2,329 | 0,6 | 3,406 | 1,124
Bagging | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Random forest | 0,184 | 0,477 | 0,960 | 536,203 | 0,205
 |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Ridge | 1,851 | 2,329 | 0,6 | 1,891 | 0
Lasso | 1,851 | 2,329 | 0,6 | 3,406 | 
Bagging | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Random forest | 0,184 | 0,477 | 0,960 | 536,203 | 0,205
Regression results (best metric per row in bold, worst underlined)
Parameters estimated using cross-validation
70-30 training-test splits

## Slide 62: REGRESSION RESULTS AND ANALYSIS
Interpretation : Non-parametric models
 | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
K-NN | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Support vector regression | 2,243 | 3,813 | 0,515 | 47,047 | 0,236
 |  |  | R² | Fitting time (s) | Inference time (ms)
K-NN | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Support vector regression | 2,243 | 3,813 | 0,515 | 47,047 | 0,236
Regression results (best metric per row in bold, worst underlined)
Parameters estimated using cross-validation
70-30 training-test splits

## Slide 63: REGRESSION RESULTS AND ANALYSIS
Interpretation : Tree-based models
 | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Decision tree | 0,521 | 0,921 | 0,887 | 0,922 | 1,053
Random forest | 0,184 | 0,477 | 0,960 | 536,203 | 0,205
Bagging | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Boosting | 0,408 | 0,799 | 0,912 | 61 | 1,643
 |  |  | R² | Fitting time (s) | Inference time (ms)
Decision tree | 0,521 | 0,921 | 0,887 | 0,922 | 
Random forest | 0,184 | 0,477 | 0,960 | 536,203 | 0,205
Bagging | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Boosting | 0,408 | 0,799 | 0,912 | 61 | 
Regression results (best metric per row in bold, worst underlined)
Parameters estimated using cross-validation
70-30 training-test splits

## Slide 64: REGRESSION RESULTS AND ANALYSIS
Interpretation : Neural networks
 | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Neural networks | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
 |  |  | R² | Fitting time (s) | Inference time (ms)
Neural networks | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Regression results (Neural network)

## Slide 65: REGRESSION RESULTS AND ANALYSIS
Hyperparameter estimation

## Slide 66: REGRESSION RESULTS AND ANALYSIS
Residual plots

## Slide 67: SIMULATIONS AND DATA GENERATION
Crack length vs health indicator
Gaussian process regression is used to estimate the crack length from the health indicator

## Slide 68: USE CASE
Predictions using a surrogate ML model
Remaining useful life estimation using a Markov chain model coupled with support vector regression as a surrogate model

## Slide 69: SIMULATIONS AND DATA GENERATION
Plasticity
Metallization layer and wire (Al) : Bilinear Kinematic Hardening :
  Yield stress σ = 29MPa
  Tangent modulus E = 35.5MPa
Copper : Chaboche Kinematic Hardening : 2 modes :
  T = 20◦C : C1 = 54.041MPa, γ1 = 962, C2 = 721MPa, γ2 = 1.1
  T = 50◦C : C1 = 52.880MPa, γ1 = 1000, C2 = 700MPa, γ2 = 1.1
  T = 150◦C : C1 = 45.760MPa, γ1 = 1100, C2 = 600MPa, γ2 = 1.1

## Slide 70: SIMULATIONS AND DATA GENERATION
Plasticity
Metallization layer and wire (Al) : Bilinear Kinematic Hardening :
  Yield stress σ = 29MPa
  Tangent modulus E = 35.5MPa
Copper : Chaboche Kinematic Hardening : 2 modes :
  T = 20◦C : C1 = 54.041MPa, γ1 = 962, C2 = 721MPa, γ2 = 1.1
  T = 50◦C : C1 = 52.880MPa, γ1 = 1000, C2 = 700MPa, γ2 = 1.1
  T = 150◦C : C1 = 45.760MPa, γ1 = 1100, C2 = 600MPa, γ2 = 1.1

## Slide 71: REGRESSION RESULTS AND ANALYSIS
Effect of quadratic features
Regular features | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Regular features |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,851 | 2,329 | 0,6 | 0,031 | 0
Regularization (linear) | 1,851 | 2,329 | 0,6 | 1,891 | 0
Tree-based | 0,175 | 0,463 | 0,962 | 673,375 | 0,211
Non-parametric | 0,475 | 0,769 | 0,897 | 0,422 | 0,010
Neural network | 0,438 | 0,829 | 0,905 | 991,062 | 0,022
Augmented features | MSE () | MAE () | R² | Fitting time (s) | Inference time (ms)
Linear | 1,647 | 2,326 | 0,637 | 0,047 | 0
Regularization (linear) | 1,647 | 2,326 | 0,637 | 2,187 | 0
Tree-based | 0,110 | 0,369 | 0,976 | 1072,156 | 0,242
Non-parametric | 0,429 | 0,737 | 0,906 | 0,688 | 0,019
Neural network | 0,275 | 0,672 | 0,939 | 953,175 | 0,018
Augmented features |  |  | R² | Fitting time (s) | Inference time (ms)
Linear | 1,647 | 2,326 | 0,637 | 0,047 | 0
Regularization (linear) | 1,647 | 2,326 | 0,637 | 2,187 | 0
Tree-based | 0,110 | 0,369 | 0,976 | 1072,156 | 0,242
Non-parametric | 0,429 | 0,737 | 0,906 | 0,688 | 0,019
Neural network | 0,275 | 0,672 | 0,939 | 953,175 | 0,018

## Slide 72: SIMULATIONS AND DATA GENERATION
Plasticity
Metallization layer and wire (Al) : Bilinear Kinematic Hardening :
  H. Lu and C. Bailey (2014) Application of nonlinear fatigue damage models in power electronic module wire bond structure under various amplitude loadings, Advances in Manufacturing
Copper : Chaboche Kinematic Hardening : 2 modes :
  Y. Liu and S. Liu (2014) Modeling and simulation of power electronic modules with microchannel coolers for thermo-mechanical performance, Microelectronics Reliability

## Slide 73: MACHINE LEARNING BEYOND REGRESSION
Transfer learning : challenge
Utilize architectures that present a clear hierarchical structure such as radial basis function networks and autoencoders

## Slide 74: REGRESSION RESULTS AND ANALYSIS
Consistent models : MSE